## Slide 1: Modeling of a “HoloLens 1”-Type Layout with Light Guide Component

## Slide 2: Abstract
Most innovative augmented and mixed reality devices nowadays are based on light-guide or wave-guide configurations in combination with microstructures to couple light in and out. VirtualLab Fusion is capable of the detailed modeling of such devices by applying our unique physical optics approach, which includes all effects of interest (e.g. coherence, polarization and diffraction). We demonstrate this capability by modeling a device with a “HoloLens 1”-type (1D-1D pupil expander) layout with a Light Guide component capable of guiding light with a 32° × 18° field of view.

## Slide 3: Modeling Task
outcoupling
incoupling
exit pupil
expansion (EPE)
Light guide
consisting of diffractive
  incoupling region
  eye pupil expansion region
  outcoupling region
source: Scanning source
FoV 32° × 18° (cartesian angles)
wavelength 532 nm
How to model a light guide that can guide a certain field of view (FoV)?
Parameters from default layout by Layout Design Tool, reference patent: WO2011107831A1.

## Slide 4: Working Principle of Light Guide
incoupling
outcoupling
In order to ‘‘trap’’ the light inside the light guide slab, total internal reflection (TIR) is used. For this purpose, gratings are applied to couple the incident light in and out and to ensure that conditions for TIR are fulfilled.
The function of the exit pupil expansion grating is to replicate the incoupled pupil in one direction (here: x direction) in order to expand the exit pupil, or in other words generate the eye box.
In this type of setup, the outcoupling grating is not only responsible for outcoupling the light toward the observer, but also for the pupil expansion in the second direction (here: y-direction).
This separated pupil expansion is characteristic of a “HoloLens 1”-type
layout.

## Slide 5: Layout Design Tool
In order to set up the lateral layout of such a light guide the Layout Design tool of VirtualLab can be used (only available with the Light Guide Toolbox Gold).
The parameters of this example correspond to the default configuration.
This tool provides an optical setup with a light guide according to the given specifications of incident light and eye box. In particular, the lateral position and extension of the grating regions as well as the grating periods are determined automatically.
After defining the parameters, click the button Create Result, and the optical setup and the corresponding k-layout diagram will be generated.
1
2
3
4
5

## Slide 6: k-layout Visualization
The following parameters can be configured:
  wavelength
  surrounding and slab material
  angular range of FoV
  grating periods & orientations
The resulting diagram contains the following information (in k domain):
Circles that depict the propagation condition (available directions and k values) inside the materials.
Extension, shape and position of FoV for impinging and diffracted light after certain grating regions.
Illustration of shifts of the FoV introduced by the gratings.
FoV box
1
2
3
4
The k-layout diagram is either created together with the light guide setup as a by-product of the Layout Design tool or it can be generated independently by the corresponding entry in the menu.
The adjustment of any parameter will change the figure accordingly.

## Slide 7: Light Guide Surface Layout
Geometric layout exhibits 3 gratings on the first plane surface:
Grating #1: incoupling grating
Grating #2: expansion grating
Grating #3: outcoupling grating
Grating #1
Grating #2
Grating #3

## Slide 8: Grating #1: Incoupling Grating
The incoupling grating is defined in a rectangular region. The general workflow to define grating regions is:
determine the shape and size of the region
select region channels

## Slide 9: Grating #1: Incoupling Grating
define the period and orientation of the grating;
specify the propagating orders (from front side and back side);
specify the transmission and reflection efficiencies;

## Slide 10: Grating #2: Expansion Grating in Simple Polygon Region
The expansion grating is defined in a polygon-shaped region.
The required region channel is ‒/+, therefore only reflected orders for light impinging on the back side of the grating are specified.

## Slide 11: Grating #3: Outcoupling Grating
The outcoupling grating is defined in a rectangular region, again.
Region channels ‒/+ and ‒/‒ are required to activate the orders responsible for expansion and outcoupling.

## Slide 12: Result: Ray Tracing in 3D System
Rays in System view with 32° × 18° scanning source input (9 modes, differently colored):
Rays in System view
with central angle of FoV:
Note: Only rays that hit the detector are displayed.

## Slide 13: Result: Field Tracing (Real Color View)
Energy density distribution at eyebox for
FoV (32° × 18°) using scanning source (9 modes):
Energy density distribution at eyebox
for central FoV mode:
Some beams hit the edge of the expansion region, causing the beam to be partially diffracted by the grating and partially totally internally reflected. This causes the segmented footprints which can be seen here.

## Slide 14: Result: Field Tracing (False Color View)
Energy density distribution at eyebox for
FoV (32° × 18°) using scanning source (9 modes):
Energy density distribution at eyebox
for central FoV mode:
The distribution of the energy density in the eye box provides an impression of the lateral uniformity for a single mode (left) and for several modes (right).

## Slide 15: Lateral Uniformity Evaluation
…
In order to evaluate the lateral uniformity in the eye box, the Uniformity Detector is provided, which can be found in the element tree (under Detectors > Merit Functions > Uniformity Detector). This detector is capable of investigating the lateral energy density distribution in a specific area (e.g., eye box) at defined positions.
Uniformity detector result at eye box for center FoV mode:
Define the shape, size and number of the evaluation pupils to distribute them in the desired area (eye box).
…
Uniformity detector result at eye box for 9 modes :
Pupil with maximum energy density is at the lower right corner of the eye box, while the minimum is at the top left corner.
maximum
minimum
resulting uniformity error

## Slide 16: Document Information
title | Modeling of a “HoloLens 1”-Type Layout with Light Guide Component
document code | USC.0238
document version | 1.2
software edition | VirtualLab Fusion Basic
software version | 2021.1 (Build 1.180)
category | Application Use Case
further reading | Construction of a Light Guide Lightguide with Butterfly Eye-Pupil Expander based on Patent by Microsoft Lightguide with 2D-Periodic Grating Structures (Diamond-Shaped) Based on Patent by Wave Optics Control of Accuracy-Speed Balance for MTF Analysis in Complex Waveguide Devices for AR-Applications

## Slide 17: Presearch
Light guide, HoloLens, grating, grating regions, polygon, region waveoptics, lightguide, waveguide, wave guide, TIR, incouple, outcouple, EPE, expansion, augmented reality, mixed reality, AR, MR,

## Slide 18: Short Abstract
This use case demonstrates the modeling of a device with a “HoloLens 1”-type layout with a Light Guide component capable of guiding light with a 32° × 18° field of view.

## Slide 19: Marketing Picture
field distribution
3D view of the layout